## Slide 1: موضوع : ویژگی های سوخت بنزین ارائه دهنده:
به نام خدا

## Slide 2: مقدمه
توسعه و تکامل این سوخت همراه با موتورهای احتراق داخلی اشتعال-جرقه ای
آلمانی
US
UK
بنزین
Gasoline
Petrol

## Slide 3: ترکیب سوخت
ارزش حرارتی بالا
عدد اوکتان بالا
داشتن بو
عدد اوکتان بالا ، ترکیبات سمی ، تشکیل دوده
15% آلکان های خطی
30% ایزوآلکان
15% سیکلوآلکان
5% آلکِن (اولفین)
35% ترکیبات آروماتیک
87% کربن و 13% هیدروژن
ترکیب سوخت به طور متوسط
درصد جرمی

## Slide 4: ویژگی های سوخت
نقطه جوش(ºC)
چگالی (kg/m^3)
Flash point(ºC)
LHV(MJ/kg)
بنزین
200-30
750
30-
42.7
گازوییل
300-200
860
40
43.4
نفت سفید
300-150
800
40
43.0
Flash point : کمترین دمایی که سوخت می تواند محترق شود

## Slide 5: ویژگی های خود اشتعالی
عدد اوکتان : مقاومت خوداشتعالی مشابه با سوخت مرجع دارای درصد حجمی ایزواوکتان ON
ماشین تراکم سریع (RCM)
Ron
Mon
Rdon
عدد اوکتان بنزین مرغوب (RON): 98-92
عدد اوکتان بنزین در ایران : معمولی 87 و سوپر 95

## Slide 6: سرعت شعله
Chart: 
| 0.78734179999999998 | 0.88354429999999995 | 1.0303798 | 1.1265822999999999 | 1.1772152 | 1.278481
Ethanole | 26.6499 | 34.6977 | 45.2393 | 47.1662 | 44.7859 | 36.398
n-Heptane | 27.465 | 35.0474 | 39.3301 | 40.9126 | 38.5949 | 32.9022
iso_Octane | 23.3862 | 29.858 | 34.2897 | 35.2025 | 34.7599 | 31.7112
Propane | 27.3699 | 35.0265 | 39.3968 | 40.6164 | 38.2741 | 32.5083
Natural gas | 26.3566 | 32.9457 | 37.4677 | 39.5349 | 38.1137 | 32.1705
Gasoline | 26.0892 | 31.8924 | 35.9815 | 37.285 | 35.1606

## Slide 7: با تشکر از توجه شما
مراجع
Fuels by Sidoro Martinez
Fuel properties by Isidoro Martinez
A rapid compression machine – design, characterization, and autoignition investigations
Laminar flame speeds of ethanol, n-heptane, isooctane air mixtures
Laminar flame speed correlations for methane, ethane, propane and their mixtures, and natural gas and gasoline for spark-ignition engine simulations